# MISSOURI DEPARTMENT OF TRANSPORTATION

#### AVIATION SECTION

# AIRPORT LAYOUT PLAN (ALP) & NARRATIVE CHECKLIST

# EFFECTIVE OCTOBER 1, 2008, ALPs ARE REQUIRED TO HAVE AN ACCOMPANYING AERONAUTICAL SURVEY IN ACCORDANCE WITH ACs 150/5300-16, 17, 18. IF THE AIRPORT ALREADY HAS COMPLETED AN AERONAUTICAL SURVEY IN ACCORDANCE WITH THE ABOVE CIRCULARS, THAT DATA IS TO BE USED FOR THE DEVELOPMENT OF THE ALP.

ALPs and/or Master Plans shall conform to this checklist as required by this office and the FAA.  Failure to include a completed and signed checklist along with the ALP and/or Narrative/Master Plan will result in rejection for review.

As stated in Order 5100.38, an ALP remains current for a 5-year period, or longer, unless major changes at the airport are made or planned.

APPLICABLE ADVISORY CIRCULARS:

Airport Master Plan, AC 150/50705-6B

## Airport Design, AC 150/5300-13, Changes 1 through 15

Airport Name & Location:

Critical Aircraft

| Existing Make: | Model: | Annual Itinerant Ops: |  |
| --- | --- | --- | --- |
| Ultimate Make: | Model: | Annual Itinerant Ops: | Forecast Year: |

Airport Reference Code (ARC)

Runway:

Runway:

Desired Approach Minimums:

| Rwy End: |  | Minimum: |  | Rwy End: |  | Minimum: |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Rwy End: |  | Minimum: |  | Rwy End: |  | Minimum: |  |

###### Included

AIRPORT LAYOUT PLAN COMPONENTS:				Yes	No

I.   Narrative Report

II.  Airport Layout Drawing

III. Airport Airspace Drawing

IV. Inner Portion of the Approach Surface Drawing

V.  Terminal Area Drawing

VI. Land Use Drawing

VII. Airport Property Map (an Exhibit A is separate from this)

VIII. Airport Departure Surfaces

### I.  NARRATIVE REPORT FOR ALP UPDATES

An ALP update with Narrative is appropriate to a full Master Plan whenever the fundamental assumptions of the previous Master Plan have not changed.  If it is determined that a more thorough analysis is needed, a full Master Plan is probably a better choice.  Please consult with the MoDOT Aviation Section office for further guidance.

Included      		Remarks

Yes   	No

| INVENTORY A brief history of the airport, how it was acquired, the airport location and accesses to the airport, any previous FAA AIP grants, the aviation and business community served by the airport, and the airport service area and why this updated is warranted. Inventory of existing airport facilities, based aircraft, history of airport operating and maintenance budget, expenditures and sources of revenues, management agreement, and land ownership and easements of record. |  |
| --- | --- |
| FORECAST AVIATION DEMAND Current, 5 yrs, 10 yrs, 20 yrs Local Operations Annual Itinerant Operations All Aircraft Current Design Aircraft Future Design Aircraft Total Annual Operations Based Aircraft Based Aircraft Mix Annual Instrument Approaches (AIA) Enplaned Passengers (Commercial Service Locations Only) |  |
| FACILITY REQUIREMENTS Assessment of facility requirements including, but not limited to: runway length, width, strength, orientation approaches, land requirements, wind analysis, taxiways, lighting, utilities, terminal areas, hangars, aprons, tie downs, etc. |  |
| ALTERNATIVES & STAGE DEVELOPMENT Basis for the proposed items of development, drawings, schedules, and project costs (CIP) |  |
| ENVIRONMENTAL Statement of environmental analysis for areas of potential impact, level of impact, & proposed mitigation. Agency contacts could be included & attached. State if proposed development would require need for an Environmental Assessment (EA) or Environmental Impact Statement (EIS). |  |
| Other – Explanation of any unique features of the airport that might require deviation from FAA design standards. |  |

### II.  AIRPORT LAYOUT DRAWING

An airport layout plan (ALP) is a graphic presentation to scale of existing and ultimate airport facilities, their location on the airport and the pertinent clearance and dimensional information required to show relationships with applicable standards.

Included         	Remarks

Yes	No

| SHEET SIZE 22" X 34" - Black Line Paper (ANSI D) minimum |  |
| --- | --- |
| SCALE 1" = 200' to 1" = 600' |  |
| NORTH POINT & DATUM REFERENCES True & Magnetic Declination & Epoch Year NAD 83 (horizontal coordinates) NAVD 88 (MSL elevations) |  |
| WIND ROSE (3 required – all weather, VFR, IFR) Source & Time Period (latest 10-year period, using 36-point) |  |
| Individual & Combined Coverage 10.5 Knots 13 Knots 16 Knots 20 Knots |  |
| AIRPORT REFERENCE POINT (ARP) Existing/Ultimate with lats and longs to nearest second. Elevations to 0.1 of a foot |  |
| TOPOGRAPHIC INFORMATION Contours 2' to 10' (light lines) |  |
| ELEVATIONS Runway Ends (nearest 0.1 ft, exist & ult) Displaced Thresholds (if any) Runway Intersections Runway High and Low Points Roadways & Railroads at points where they intersect Approach Surface & extended runway centerline Structures on Airport (if no Terminal Drawing) |  |
| LINES ILS/MLS Critical Areas (GS & LOC) AWOS/NDB Critical Areas Building Restriction Lines (BRL) Building Height for BRL (35’ typical) Property Lines (exist & ult) Section Corners Survey Monuments (PACS/SACS) Runway Visibility Zones |  |

II. ALD (CONT'D)

Included         	Remarks

Yes	No

| RUNWAY DETAILS Length and Width (exist & ult) End Numbers True Bearing (nearest .01 degree) End Coordinates (nearest .01 sec) Markings (exist & ult) Lighting Symbols (threshold only, exist & ult) Clearways & Stopways/Overruns Safety Areas (RSA, OFA, OFZ, etc.) Include dimensions |  |
| --- | --- |
| TAXIWAY DETAILS Width Clearance to Runway Clearance to Aircraft Parking Clearance to Objects Hold Position markings/signage (exist & ult) |  |
| APRON Location Aircraft Parking |  |
| RUNWAY PROTECTION ZONES Dimensions (exist & ult) Type of Ownership (Fee or Ease) |  |
| APPROACHES Approach Surface Slope & Type (exist & ult) |  |
| TITLE AND REVISION BLOCK |  |
| MODOT DISCLAIMER (cover page only) State Version Federal Version |  |
| APPROVAL BLOCK-(SPONSOR ONLY) |  |
| AIRPORT DATA TABLE Airport Elevation (nearest 0.1 ft) ARP Coordinates (nearest second) Airport Electronic Aids (NDB/VOR/Beacon) Mean Max Temp. (Hottest Month) Airport Reference Code (ARC) Critical Design Aircraft (exist & ult) |  |
| BUILDING TABLE (See ALP Guidance) |  |
| LEGEND TABLE |  |

II. ALD (CONT'D)

Included		Remarks

Yes   	No

| RUNWAY DATA TABLE (existing & ultimate) Approach Category and Design Group Runway (length/width) Percent effective gradient (max) Percent wind coverage Runway Lighting (LIRL, MIRL, HIRL) Runway Marking (V, NP, or P) Pavement Material Pavement Design Strength (exist & ult critical aircraft) (#lbs – S, D, DT, DDT) Runway Safety Area (length/width) Object Free Area (length/width) Obstacle Free Zone (length/width) Taxiway Width Taxiway Lighting For each runway end (exist & ult): Approach Surface Slope Electronic Aids (Localizer, Glide Slope, etc) Visual Aids (REIL, VGSI, etc) Approach Visibility Minimums (V, 1 mile, 3/4 mile,1/2 mile, CAT II, CAT III) Part 77 Approach Use Type Aeronautical SurveyType Required for Approach Touchdown Zone Elevation (TDZE) (highest runway elevation within first 3,000 ft) Takeoff Run Available (TORA) Takeoff Distance Available (TODA) Accelerate Stop Distance Available (ASDA) Landing Distance Available (LDA) |  |
| --- | --- |
| MODIFICATION TO AIRPORT DESIGN STANDARDS TABLE Approval Date, Airspace Case No. Standard Modified, Description If No Standard Modified, State “None Required” |  |
| OBSTACLE FREE ZONE (OFZ) OBJECT PENETRATIONS TABLE If none, state “No OFZ Penetrations” |  |
| THRESHOLD SITING SURFACE OBJECT PENETRATIONS TABLE If none, state “No TSS Penetrations” The TSS lines does not need to be shown if there are no obstructions. |  |

###### ADDITIONAL ALD COMMENTS

### III.  AIRPORT AIRSPACE DRAWING

Included         	Remarks

Yes   	No

| ZONING/ORDINANCE STATEMENT: Include the following text (if there are not zoning/ordiances) in a bold and prominent location on the drawing to catch the reader’s attention. If zoning and/or ordinances exit, please identify this on the drawing. For NPIAS Airports: “Per Federal Grant Assurances #20 and #21, the City/County of ________ should, at a minimum, enact height and hazard zoning and/or ordiances based on Federal Aviation Regulation Part 77 Surfaces in order to protect and prevent development of airport hazards both on and around the airport and especially in the approach and departures areas of the runway to the extent possible.” For Non-NPIAS Airports: “Per State Grant Assurances, the City/County of ________ should, at a minimum, enact height and hazard zoning and/or ordiances based on Federal Aviation Regulation Part 77 Surfaces in order to protect and prevent development of airport hazards both on and around the airport and especially in the approach and departures areas of the runway to the extent possible.” |
| --- |
| PLAN VIEW Current USGS 7 1/2 Minute Quad. Runway Numbers (ultimate only) Part 77 Imaginary Surfaces Elevation Contours (even 50' intervals on sloping surfaces) Scale (1" = 2000'- 3000') Show Part 77 Subpart C Obstructions beyond RPZ in Obstruction Data Table |  |
| APPROACH PROFILES (Existing and Ultimate) Scale (1" = 1000' H, 1" = 100' V for Visual & Non-Precision Rwys) Scale (1" = 2000' H, 1'= 200' V for ILS Runways) for a composite ground profile along extended runway centerline Significant Objects Top Elevation of Significant Objects Part 77 Approach Slope Profile |  |
| OBSTRUCTION TABLE (BEYOND INNER APPROACH SURFACE) Shall contain: Obstruction Identification Number Description/Type of Object/Obstruction Obstruction Lat/Long Obstruction AGL Elevation Obstruction MSL Elevation For Roadways/Railroads, show Part 77 Obstruction Height Penalty Amount of Penetration & Part 77 Surface Obstructed Disposition of Obstruction |  |

###### ADDITIONAL COMMENTS FOR AIRPORT AIRSPACE DRAWING

### IV. INNER PORTION OF THE APPROACH SURFACE DRAWING

Included         	Remarks

Yes   	No

| PLAN VIEW (Existing & Ultimate) (out to 100’ above rwy elevation for the approach slope) USE AERIAL PHOTOGRAPH AS BASE MAP Scale (1" = 200') Property Line Signficant Objects Identified by Number Clearance over Roads, Railroads at Centerline & Edge of Approach Surface (Include Road/Railroad Elev.) Runway End Number and Elevation Ground Contours (light lines) Runway Safety Area Object Free Area Runway Protection Zone (RPZ) Precision Object Free Area (POFZ) |  |
| --- | --- |
| PROFILE VIEW Scale (1" = 200'H, 1" = 20'V) Terrain Along Extended Centerline of Runway (out to 100’ above rwy elevation for approach slope) Significant Objects Cross-Section of Roads & Railroads Obstructions Identified by Number (same as used on plan view) |  |
| RUNWAY CENTERLINE PROFILE Scale (vertical sufficient to show line of sight req.) Elevations (stations and elev at runway ends and at all points of grade change) |  |
| OBSTRUCTION TABLE (both existing & ultimate) Separate Table for each Approach Surface Obstruction Identification Number Obstruction Elevation Part 77 Obstruction Height Penalty Top Elevation of Objects Description of Obstruction Amount of Penetration & Surface Obstructed Disposition of Obstruction |  |

ADDITIONAL COMMENTS

V. TERMINAL AREA DRAWING

Included         	Remarks

Yes   	No

| Scale ( 1" = 50' to 1" = 100') Show all clearance dimensions between runway, taxiway, and taxilane centerlines and hangars, buildings, aircraft parking, and other objects as applicable. Legend Property Line Bldg Restriction Line Apron T-Hangars Aircraft Parking Top Elevation of Structure Building Identification Table Auto Parking Areas Entrance Road |  |
| --- | --- |

###### ADDITIONAL COMMENTS

##### VI.  LAND USE DRAWING

##### NOTE:  Use ALD as a base map

Included         		Remarks

Yes   	No

| ZONING/ORDINANCE STATEMENT: Include the following text (if there are not zoning/ordiances) in a bold and prominent location on the drawing to catch the reader’s attention. If zoning and/or ordinances exit, please identify this on the drawing. For all airports: “Per State and Federal Grant Assurances, the Airport Owner will take appropriate action, including the adoption of zoning laws, to the extent reasonable, to restrict the use of land adjacent to or in the immediate vicinity of the airport to activities and purposes compatible with normal airport operations, including landing and takeoff of aircraft. In addition, if the project is for noise compatibility program implementation, it will not cause or permit any change in land use, within its jurisdiction, that will reduce its compatibility, with respect to the airport, of the noise compatability measures upon which federal and state funds have been expended.” |
| --- |
| Legend On-Airport Land Use (exist & ult) Off-Airport Land Use (exist & ult) to at least 65 DNL Contour Public Facilities Crop Restriction Lines Airport Property Lines (ultimate) Identify zoning restrictions (as applicable) |  |

###### ADDITIONAL COMMENTS

##### VII. AIRPORT PROPERTY MAP

##### NOTE:  Use ALD as a base map. An Exhibit A Property Map may be substituted for the Airport Property Map, but it is NOT recommended.  IF an Exhibit A Property is used in lieu of the Airport Property Map, it must be prepared in accordance with AC 150/5100-17.  Contact this office for further guidance.

Included         	Remarks

Yes   	No

| LEGEND |  |
| --- | --- |
| DRAWING DETAILS (existing and ultimate) Airport Features (use ALD) Property Lines (fee) Property Interest Areas (easement) Tract Boundary Line with Identification number |  |
| DATA TABLE Tract Identification Number Date of Acquisition Type of Acquisition Federal Aid Project Number Property Interest (fee or ease) Acreage |  |

###### ADDITIONAL COMMENTS

VIII. Airport Departure Surfaces

40:1 for Instrument Procedure Runways

62.5:1 for Commercial Service Runways

Included         	Remarks

Yes   	No

| PLAN VIEW (Existing & Ultimate) (out to 10200’ beyond Runway threshold for 40:1) (out to 50000’ beyond Runway threshold for 62.5:1) Scale (1" = 1000' for 40:1/ 1”=2000’ for 62.5:1) Property Lines Objects Identified by Number Runway End Number and Elevation Ground Contours (light lines) |  |
| --- | --- |
| PROFILE VIEW (Existing & Ultimate) Scale (1" = 50'V for 40:1, 1”=100’ for 62.5:1) Terrain Along Extended Centerline of Runway Significant Objects Cross-Section of Roads & Railroads Objects Identified by Number (same as used on plan view) |  |
| OBSTRUCTION TABLE Separate Table for each Runway End Object Identification Number Object Elevation Description of Objects Amount of Penetrations Disposition of Obstruction |  |

###### ADDITIONAL COMMENTS

### SIGNATURE BLOCK

The ALP and/or Master Plan/Narrative was prepared in accordance with the applicable standards and requirements and that the forgoing items are accurate as marked. Prepared By: _________________________________________Date: __________________ Signature Typed or Printed Name of Preparer: Reviewed By: ________________________________________Date: __________________ Signature Typed or Printed Name of Reviewer:

# Comments

Mag Dec is the difference between true north and mag north.  Show magnetic variation value for the closet epoch year.  Do not show the current year value unless it is an epoch year.  Do not show values for older epoch years. Obtain epoch year value by sending email to magvar@faa.gov.

Only if rwy is IFR, otherwise one rose will suffice for visual runway airports. Data can be obtained from NOAA National Data Centers. 828-271-4800.  Ask for data that be inputed into the FAA Wind Analysis Program.

Any wind data before the 1990-2000 time period is out of date.

When showing these facilities, show the critical area boundaries.  For the NDB, a 100’ radius circle should be placed around the NDB.  Metal buildings, power lines or metal fences should be kept a minimum of 100’ away from the NDB antenna.  For the AWOS, show both the 1,000’ and 500’ circle radius and define the height limitations and restrictions within each radius.  Reference FAA Order 6560.2B.

Show the BRL that is within the area portion of airport shown.  The BRL identifies suitable building area locations on airports.  This should be located where the Part 77 surfaces are at 35’ above the airport elevation unless a different height is coordinated with MoDOT.

Show locations of all established survey monuments located on or near the airport property. Identify Primary and Secondary Airport Control Stations (PACS/SACS) if they exist.  Reference AC 150/5300-16.

DO NOT USE the Airport Design software to determine runway dimensions.  Use AC 150/5325-4.

Use this language: The preparation of this document may have been supported, in part, through the State Aviation Trust Fund (Project Number___) as provided under Chapter 305, Section 305.230 RSMO.  The contents do not necessarily reflect the official views or policy of the Missouri DOT.  Acceptance of this report by the Missouri DOT does not in any way constitute a commitment on the part of the State of Missouri to participate in any development depicted therein nor does it indicate that the proposed development is environmentally acceptable or would have justification in accordance with appropriate public laws.

Use this language: The preparation of this document may have been supported, in part, through the Airport Improvement Program (Project Number___) as provided under Title 49 U.S.C., Section 47104.  The contents do not necessarily reflect the official views or policy of the FAA or the Missouri DOT.  Acceptance of this report by the FAA and Missouri DOT does not in any way constitute a commitment on the part of the United States or the State of Missouri to participate in any development depicted therein nor does it indicate that the proposed development is environmentally acceptable or would have justification in accordance with appropriate public laws.

All buildings on the ALD should be identified in alphanumeric character.  List these identifiers in a table and give a description of the structure.  If no terminal drawing is done, also include the top of structure elevation in MSL.  If any of the structures violate any airport or approach surfaces, give an ultimate disposition to correct the violation.

List the max longitudinal grade of each runway centerline.  See Chapter 5, AC 150/5300-13.

This is the Part 77 surface slopes - 20:1, 34:1, 50:1

Visual, Non-Precision, Precision

List the type of aeronautical survey required for the visibility minimums given.  See AC 150/5300-18.

Only list declared distances if it is being proposed, otherwise show “NA” for each.  It is very unlikely that a GA airport will need to utilize declared distances.  Consult with this office if this method is being considered.

This drawing shall depict those obstructions as defined in Subpart C – Obstruction Standards of FAR Part 77.   Show all obstructions to those surfaces in 77.23 and 77.25.  Source of data is through subscription to FAA’s Digital Obstacle Files and online at http://oeaaa.faa.gov.  The planner will need to evaluate all the obstructions for existing and ultimate conditions.  An existing object that has been previously studied by the FAA could very well be an impact to the proposed development or could impact other air traffic surfaces.  All obstruction data is to be presented in an Obstruction Table and reflected in both the Plan View and Approach Profile Drawings.  The Obstruction Table is to contain the following: identifier (alphanumeric or numbering), type of obstruction, lat/long, AGL elevation, MSL elevation, surface obstructed (imaginary surfaces or 77.23 surfaces), a disposition column.  Leave the disposition column empty until the FAA completes the evaluation of obstructions, which will contain the disposition for objects in order to accomplish proposed development.  The planner will then input the disposition from the FAA study into the Part 77 Obstruction Table Drawing when directed by MoDOT.  For questions, please contact our office.

Use the most current USGS Quadrangle(s) as a base map for the airspace drawing.

Show the extents of the Part 77 surfaces.  For airports that have precision approach runways show balance of the 40,000’ approach on second sheet.

See below

Depict the ground profile along the extended runway centerline representing the composite profile, based on the highest terrain across the width and along the length of the approach surface.

See also below for obstruction table.  Identify all significant objects (roads, rivers, railroads, towers, poles, etc.) within the approach surfaces, regardless of whether or not they are obstructions.  Use the objects’ same alphanumeric identifier for that used on the plan view.

This is the MSL elevation PLUS the Part 77 height penalty where applicable.  These elevations and alphanumeric identification need to remain consistent in all views.

List each object by the same alphanumeric symbol used in the plan view.

Reference Part 77 Section 77.23(b).  For this show elevation of roadway/railroad bed, then show penalty height, then show overall AGL height.

The disposition column remains blank (unless it’s an obvious and easy obstruction to show removed or mitigated) otherwise, for tall structures, leave blank as the airspace study will indicate the disposition and then that disposition will be included in the column for that obstruction in the final drawing set.

Drawings containing the plan and profile view of the inner portion of the approach surface to the runway and a tabular listing of all surface penetrations.  The drawing will depict the obstacle identification approach surfaces contained in Part 77.  The drawing may also depict other surfaces, including the threshold-siting surface, Glideslope Qualification Surface (GQS), those surfaces associated with TERPS or any other required surface as requested by the agency.  The extent of the approach surface and the number of airspace obstructions shown may restrict each sheet to only one runway end or approach.  The Plan and Profile Views must line up together for ease of readability.

Identify all significant objects (roads, rivers, railroads, towers, poles, etc.) within the approach surfaces, regardless of whether or not they are obstructions.  The same identification process as identified for the Part 77 Drawings should be used throughout all drawings, where applicable.

Show elevation information for the traverse ways’ centerline elevation where they intersect the Part 77 approach surfaces both existing and ultimate.  These elevations are to include the Part 77 height penalty and should be denoted, as a minimum, in the Obstruction Table.

Show ground contour lines in 2’, 5’, or 10’ intervals.  Topographic issues may be important in the alternatives analysis, which may require that reduced contour intervals be used.

Depict the ground profile along the extended runway centerline representing the composite profile, based on the highest terrain across the width and along the length of the approach surface.

This should match those in the plan view.

This may be shown on the Inner Portion of the Approach Surface Drawing if there is space to show the runway and RSA in sufficient detail, otherwise a separate sheet will be required.  At a minimum, this drawing is sto show the full length of the runway and RSA including runway elevations, runway and RSA gradients, all vertical curves, and a line of representing the 5’ line of sight.  See AC 150/5300-13, Chapter 5.

Follow the same guidance as identified for the Part 77 Drawing Obstruction Table.

Reference Part 77 Section 77.23(b)

Show the BRL that is within the area portion of airport shown.  The BRL identifies suitable building area locations on airports.  This should be located where the Part 77 surfaces are at 35’ above the airport elevation unless a different height is coordinated with MoDOT.

For further assistance, reference AC 150/5300-13 and Engineering Brief No. 75.  Apron size should be in correlation to forecasts.

Show proposed tie-down layout on the apron area as well as taxilane marking plan. Reference AC 150/5300-13, AC 20-35, and AC 150/5340-1.

All buildings should be identified by an alphanumeric character.  List these identifiers in a table and give a description of the building and top of structure elevation in MSL.  If any structures violate any airport or approach surfaces give an ultimate disposition to remedy the violation.

Label existing and ultimate on-airport property by usage e.g. “Terminal Area”, “Air Cargo”, “Public Apron”, “Airfield – Movement”, “Airfield – Non-movement,” etc.  Include existing and future airport features. (replicate ALD features).

Label existing and ultimate off-airport property by usage and zoning, e.g. Agricultural, Industrial, Residential, Commercial, etc.

For small GA airports, this will most likely not be needed.

Identify public facilities e.g. schools, parks, etc.

This drawing depicts the airport property boundary, the various tracts of land that were acquired to develop the airport, and the method of acquisition.  If any obligations were incurred as a result of obtaining property, or an interest therein, they are to be noted.  Obligations that stem from Federal grant or an FAA-administered land transfer program, such as surplus property programs, are to be shown.  The drawing should also depict easements beyond the airport boundary.  An airport property map is not a substitute for an Exhibit A.

Show the existing and ultimate tract/parcel boundaries of all land owned in fee by the airport and the existing and ultimate tract/parcels boundaries of all land in which the airport has an easement interest.  Identify each tract/parcel using an alphanumeric character.

List each tract by the same alphanumeric symbol used in the drawing.

E.g. surplus property, local purchase, condemnation, federal grant, etc.

List whether the property is owned in fee or if just controlled through an easement.  Specify what type of easement (aviation, air, etc.)

List the size of the tract/parcel to the nearest 0.01 of an acre.

Do not show future development encroaching departure surfaces unless it is clear as departure minimums may be affected.  Identify all significant objects within the departure surfaces, regardless of whether or not they are obstructions using an alphanumeric system.

Show ground contour lines in 2’, 5’, or 10’ intervals.  Topographic issues may be important in the alternatives analysis, which may require that reduced contour intervals be used.

Depict the ground profile along the extended runway centerline representing the composite profile, based on the highest terrain across the width and along the length of the departure surface to extents of the surface dimensions.

List each object by the same alphanumeric symbol/character used in the above views.

List the AGL height and the top of object elevation in MSL for each object.